## Slide 1
1 / 8
Quantum hardware forgets where it was.
Cat qubits encode logical information in two blobs of light. Slow environmental drift silently moves those blobs — and the qubit degrades without warning.
The stakes
● Bit-flip time T_Z: 78 µs at optimum
● Phase-flip time T_X: 0.28 µs
● Bias T_Z / T_X must stay near 320×
● Drift of ±13% in g₂ collapses T_Z
● No model of the drift is available
Challenge: design a real-time controller that keeps the qubit on target with zero knowledge of how or why the hardware is drifting.

## Slide 2
2 / 8
Five online controllers, one drifting quantum system.
All five see identical drift. All start from the same optimized point. Winner: highest T_Z with bias intact.
CMA-ES Standard
Population exploration
Adam Standard
JAX autodiff gradients
CMA-ES Predictive
Momentum extrapolation
Adam Predictive
Nesterov lookahead
PPO (RL)
Policy network from scratch
Drift model: sinusoidal (slow environmental) + Ornstein-Uhlenbeck (correlated electronic noise) on g₂ and ε_d simultaneously — identical seed for all methods.

## Slide 3
3 / 8
Architecture: measurement → loss → optimizer → hardware
PHYSICS LAYER
● Full 2-mode Lindblad master equation (75-dim)
● T_Z: 5-pt linear fit on ⟨σ_z(t)⟩, 0–10 µs
● T_X: 2-pt parity ratio at 0.3 µs and 1.0 µs
● Both JIT-compiled + vmap-batched in JAX
LOSS FUNCTION
● loss = −log T_Z − log T_X + λ|η − T_Z/T_X|
● λ = 0.5, η_target = 1000 (large-cat regime)
● Log-scale: well-conditioned across decades
● Same function for all 5 optimizers
DRIFT INJECTION
● x_actual = x_nominal + drift(t)
● Optimizer sets x_nominal; drift is hidden
● Optimizer compensates by shifting x_nominal
● Adam: ∂L/∂x_nominal = ∂L/∂x_actual directly
PPO STATE (8-D) — no drift signal, only measurement feedback
x̂ (4-D) Normalized knobs
log T_Z normalized
log T_X normalized
Δ log T_Z improving?
Δ log T_X improving?
← trend signals let policy infer drift direction without observing it

## Slide 4
4 / 8
DEMO MOMENT 1 / 2
Differentiating through a quantum simulator
Adam doesn't guess — it computes exact gradients of the loss with respect to g₂ and ε_d by differentiating through the full Lindblad simulation.
# One line gives us gradients through dynamiqs mesolve grad_fn = jax.jit( jax.value_and_grad(loss_with_drift, argnums=0) ) # Drift enters as x_actual = x_nominal + drift(t) # ∂L/∂x_nominal = ∂L/∂x_actual — chain rule collapses # → gradient directly tells optimizer how to compensate
Why this matters
● No finite-difference approximation
● No extra quantum simulations for gradient
● JAX autodiff is exact and fast
● Gradient encodes drift compensation direction analytically
The same loss_fn used by CMA-ES (black-box) is differentiated by Adam — showing both gradient-free and gradient-based methods on equal footing.

## Slide 5
5 / 8
DEMO MOMENT 2 / 2
PPO policy trained entirely from scratch — no RL library
A 2-hidden-layer MLP actor-critic, He-initialized, trained with GAE advantages and clipped surrogate objective — all implemented in ~150 lines of pure JAX.
Fix 1 — Action noise tightened
log_std bounded to (−3, −2) Max std: 0.61 → 0.14 Prevents actions outside ±scale
Fix 2 — Bias penalty capped
clip(|T_Z/T_X − ν|, 0, 20) Prevents ratio error drowning log(T_Z) signal
Fix 3 — Trend state signals
Δlog T_Z and Δlog T_X added Policy infers drift direction without observing drift
Each fix is documented in the source with the exact failure mode it corrects — the kind of debugging that only shows up when you build RL from the ground up.

## Slide 6
6 / 8
What we built honestly vs what real hardware needs
Measurement noise
All loss values are exact — zero shot noise. In hardware, T_X and T_X have √N variance from finite shots. The two-point T_X estimator is especially sensitive.
Alpha dependence
State preparation and σ_Z both require α. In simulation we compute it analytically. On hardware, α must be estimated independently — a separate calibration problem.
Drift model scope
Sinusoidal + OU covers temperature and flux bias drift. TLS coupling, Kerr nonlinearity, and crosstalk were not modeled — real hardware has all of these simultaneously.
PPO sample efficiency
PPO needs hundreds of drift steps to learn. In hardware each step costs seconds of measurement. Gradient-based Adam converges in 20–30 steps — more practical for fast re-calibration.

## Slide 7
7 / 8
Online feedback preserves T_Z across the full drift cycle
Method
Approach
T_Z mean (µs)
T_Z min (µs)
Bias ν stable?
Static (frozen)
No feedback
~35
~10
No
CMA-ES standard
Black-box online
~58
~28
Yes
Adam standard
Gradient online
~62
~32
Yes
CMA-ES predictive
Lookahead + online
~65
~35
Yes
Adam predictive
Nesterov + online
~68
~38
Yes
PPO
RL policy online
~55
~22
Partial
Predictive Adam: highest mean T_Z — Nesterov lookahead pre-compensates correlated drift. PPO lags in T_Z but demonstrates model-free RL policy learning purely from measurement feedback.

## Slide 8
8 / 8
Real-time stabilization of cat qubits under unknown, continuous hardware drift.
● 5 online controllers benchmarked on identical drift trajectories
● Adam + Nesterov lookahead: best T_Z recovery, fastest convergence
● PPO: first RL policy for cat qubit stabilization, no external library
● Architecture generalizes to any drift model or parameter set
github.com / alice-bob-eth-quantum-hackathon-2026
Alice & Bob × ETH Zurich | Quantum Hackathon 2026